## Slide 1
Week 2
Messaging
Part 1
DCS, SMCS
Internet of Things
IoT
Faisal Iradat

## Slide 2: Topics
Basics of IoT Wireless Networking
  Describe and compare the major protocols
  Discuss how they can be used in the IoT space

## Slide 3: IoT Protocols
Protocols are a set of rules for transmitting data between electronic devices according to a preset agreement regarding information structure and how each side will send and receive data.
IoT protocols are standards that enable the exchange and transmission of data between the Internet and devices at the edge.
IoT protocols can be divided into two categories
  IoT network protocols
    Provide methods of connecting IoT edge devices with other edge devices or the Internet
  IoT data protocols.
    Focus on information exchange

## Slide 4: IoT Network Protocols
Wi-Fi
LTE CAT 1
LTE CAT M1
NB-IoT
Bluetooth
ZigBee
LoRaWAN

## Slide 5: IoT Data Protocols
AMQP
MQTT
HTTP
CoAP
DDS
LwM2M
Details in the next class

## Slide 6: Application Layer Protocols
Rapidly increasing IoT devices
  Magnitude and rate at which data is generated
Challenge
  Finding and deploying messaging protocols that exchange messages more efficiently
  Application layer protocols are considered as the underlying layers used by applications
    Defining the structure of message exchanges
    How they can be transmitted

## Slide 7: Communication / Middleware Protocols
Commonly used in the deployment of IoT applications
  HyperText Transfer Protocol (HTTP)
  Message Queuing Telemetry Transport (MQTT)
  Advanced Message Queuing Protocol (AMQP)
  Constrained Application Protocol (CoAP)
  Extensible Messaging and Presence Protocol (XMPP)
  Data Distribution Service (DDS)
  Among others
Features
  Similar features in terms of connectivity
  Vary in the degree to which these features are offered

## Slide 8: Choosing the protocol
Challenge
  Consider the hardware characteristics of IoT devices
  type of data link layer protocols employed
  bandwidth they support
    IoT devices do not use a universal radio technology
    Data rate varies considerably depending on the size and hardware components used to build these devices
Example
  Low-rate wireless personal area networks (LR-WPANs)
    Leverage IEEE 802.15.4 PHY
    Data rates up to 250 Kbps
    Packet length of approximately 127 bytes

## Slide 10: HTTP
A common request header size in HTTP
  For example user-agent
    700-800 bytes
Uncompressed request header
  200 bytes to more than 2KB
Application layer protocols that are capable of capturing data much faster than actual physical data rates often leads to high latency.
Support for protocols that can accommodate physical data rates at the data link layer

## Slide 11: Lightweighted Protcols
IOT devices producing data at a high velocity often require
  Lightweight communication protocols e.g.
    Battery-supported IoT temperature device programmed to send localized temperature readings at a fixed frequency (e.g. every 10 seconds) to an IoT hub (e.g. Microsoft Azure IoT Hub)
    HTTP not a feasible option
  Alternate
    Message Queuing Telemetry Transport (MQTT)
    Smallest packet size is 2 bytes compared to 200 bytes HTTP MQTT is a Machine-to-Machine (M2M)

## Slide 12: Performance
Significantly influenced by the choice of messaging protocol
  Employing a suitable messaging protocol that
    Reduce network traffic and latency
    Increases IoT application’s reliability
No universal protocol that can be used across heterogeneous IoT environments
Choice - Messaging protocol depends
  IoT application’s business requirements
  Software capabilities
  Device or hardware capabilities
  Average size of data exchanges, among many others
Focus messaging or middleware protocols that are commonly used in deploying IoT systems

## Slide 13: IoT MESSAGING PROTOCOLS
Traditional IoT cloud architecture
  IoT devices relocate to the cloud for data accumulation (i.e. storage) and abstraction (i.e. aggregation and access).
IoT edge-based architecture
  Reduces the amount of data in which only partial data relocates to the cloud for further storage and processing
  Network and system architectures are generally responsible for not only collecting data at the edge of the network but also performing advanced functions such as
    Data analysis and processing.
Data accumulation and abstraction partially shift from the cloud to the edge of the network
  Significantly contributes to reduction in network traffic as the number of IoT devices increases.

## Slide 14: IoT edge-based

## Slide 15: A communication-centric IoT reference model (CIoT)

## Slide 18: Messaging Protocols
Messaging protocols that support IoT data exchange
  Device-to-Device (D2D) where communication is provided between two nodes or devices directly.
  Device-to-Application (D2A) where communication is performed between devices and an IoT application.
  Device-to-Gateway (D2G) where communication is provided through a gateway that resides in close proximity to the edge of the network while interacting with IoT devices.
  Device-to-Cloud (D2C) where communication is achieved directly between IoT devices and cloud service providers.

## Slide 19: SUPPORT FOR IoT MESSAGING PROTOCOLS ON THE CLOUD

## Slide 21: HTTP
Application-level, generic, stateless protocol
Used generally for data communication over the World Wide Web
HTTP is content negotiation of data representation
  Enables different heterogeneous devices built independently of the data to be shared

## Slide 22: CONSTRAINED APPLICATION PROTOCOL (CoAP)
A web transfer protocol that is intended for devices running on constrained (e.g., low-power, lossy) networks
Constrained devices
  8-bit microcontrollers
  Small amount of memory
Designed for Machine-toMachine (M2M) applications
  Factory automation
  Smart energy
Similar to HTTP, CoAP is a request-response interaction model and uses major concepts from the web such as Uniform Resource Identifiers (URIs) and Internet media types
CoAP aims to bridge HTTP and RESTful services through simple interfacing.
  Quick exercise:
    What are REST and RESTful services

## Slide 24: CoAP Methods

## Slide 25: CoAP Message

## Slide 26: CoAP Message Exchange

## Slide 27: IoTivity
Open source software framework that enables device-to-device communication, uses CoAP as its application layer

## Slide 28: MQTT
Need for a lightweight protocol that is designed to handle situations in cases of unreliable networks or intermittent connectivity
MQTT
  MESSAGE QUEUING TELEMETRY TRANSPORT
  OASIS standard
  Publish-subscribe lightweight messaging protocol designed for constrained devices
  Enabling the exchange of data with the cloud in a realtime manner
MQTT, an application layer protocol designed for Machine-to-Machine (M2M)
  Uses a publish-subscribe model
  Runs on top of the Transmission Control Protocol

## Slide 29: MQTT Message

## Slide 30: Centralized Broker Model

## Slide 31: QoS

## Slide 32: Support

## Slide 33: Scenario

## Slide 34: eMQTT, HiveMQ, Moquette

## Slide 35: MQTT and CoAP