## Slide 1: IoT Session 11
Dr Faisal Iradat

## Slide 2: LAN
Local Area Networks, or LANs, are the “physical” networks that provide the connection between machines
  home, school or corporation
LANs are, as the name says, “local”
IP (Internet Protocol), layer that provides an abstraction for connecting multiple LANs into the Internet
TCP deals with transport and connections and actually sending user data

## Slide 3: Layered Model
Four-layered model
  Application; Transport; Network; Link
  Each layer can be perceived as a programming interface or library
    Similar to function calls
    A layer can communicate directly with one above or below it

## Slide 4: Link Layer
In charge of actual delivery of packets
Conceptually subdivided
  Physical layer
    analog electrical, optical or radio signaling mechanisms
  Logical Layer
    all the digital (non-analog – operations on packets)
Application
Transport
Network
Logical
Physical

## Slide 5: Internet five-layer Model
Physical/logical division gives us the Internet five-layer model
Less a formal hierarchy as an ad hoc classification method

## Slide 6: Data Rate, Throughput and Bandwidth
Data Rate
  rate at which bits are transmitted
Throughput
  overall effective transmission rate
  measured at a higher network layer than the data rate
Bandwidth
  Refer to either data rate or throughput
  Synonym for data rate
Goodput
  refer to what might also be called “application-layer throughput”
  amount of usable data delivered to the receiving application
  retransmitted data is counted only once
  retransmitted data counted twice under some interpretations of “throughput”

## Slide 7: Packets
Modest-sized buffers of data
  transmitted as a unit through some shared set of links
Prefixed with a header
  delivery information
Common case known as datagram forwarding
Header
  destination address
  headers in networks using so-called
Virtual-circuit forwarding contain instead an identifier for the connection
Networking today is packet-based
Circuit switched – telephony network

## Slide 8: Header
LAN layer
  Packets can be viewed as buffer
  Packets are often referred to as frames at the LAN layer
  Segments at the Transport layer

## Slide 9: Packet Size
Ethernet
  Maximum of 1500 bytes of data. By comparison, TCP/IP packets
  MTU (Max. Trans. Unit) is 1500 bytes
    Largest IP packet (or some other payload) an Ethernet frame can contain is 1500 bytes
    Additional 26 bytes for the Ethernet header results in a maximum frame (not the same as MTU) of 1526
TCP/IP packets originally often held only 512 bytes of data
Token Ring packets could contain up to 4 kB of data.
Proponents of very large packet sizes, larger even than 64 kB
ATM (Asynchronous Transfer Mode) protocol uses 48 bytes of data per packet

## Slide 10: Packet Size Contd…
Ethernet headers
  14 bytes
IP headers
  20 bytes
TCP headers
  20 bytes
Lets say if TCP connection sends 512 bytes of data per packet, then the headers amount to _______% of the total
Voice-over-IP
  160 bytes of data
  54 bytes of headers
  making the header about _______% of the total
  Compressing the 160 bytes of audio, however, may bring the data portion down to 20 bytes, meaning that the headers are now ___% of the total
Notes: 10% [54/(34+516)]
25% [54/(160+54)]
73% [54/(54+20)]

## Slide 11: VoIP
RTP (Realtime Transfer Protocol) header: 12 bytes
UDP (User Datagram Protocol) header: 8 bytes
IP (Internet Protocol) header: 20 bytes
Ethernet header: 14 bytes

## Slide 12: Datagram
RFC 1594 defines the term Datagram as follows:
“A self-contained, independent entity of data carrying sufficient information to be routed from the source to the destination computer without reliance on earlier exchanges between this source and destination computer and the transporting network.”

## Slide 13: Datagram Forwarding
Packet headers contain a destination address
Switches or routers
  look at this address and get the packet to the correct destination.
Datagram forwarding
  Providing each switch with a forwarding table <destination, next_hop> pairs.
    looks up the destination address (presumed globally unique) in its forwarding table
    finds the next_hop information: the immediate-neighbor address to which the packet should be forwarded
    bring it one step closer to its final destination.
  The next_hop value in a forwarding table is a single entry
Switches delivers the packet, one hop at a time, to its ultimate destination
IP routing
  table “destination” entries will correspond to prefixes of IP addresses
    Huge savings in space
Fundamental
  Switch can perform a lookup operation

## Slide 14: Example

## Slide 15: Example Contd…

## Slide 16: Example Contd..

## Slide 17: Datagram Forwarding
Datagram Forwarding
  each packet is forwarded “in isolation”
  switches involved do not have any awareness of any higher-layer logical connections
  also called stateless forwarding
RFC 1122
To improve robustness of the communication system, gateways are designed to be stateless, forwarding each IP datagram independently of other datagrams. As a result, redundant paths can be exploited to provide robust service in spite of failures of intervening gateways and networks.
The fundamental alternative to datagram forwarding is virtual circuits

## Slide 18: Virtual Circuits
Each router maintains state about each connection passing through it
Different connections can be routed differently
Datagram forwarding is sometimes allowed to use other information beyond the destination address
  In theory, IP routing can be done based on the destination address and some quality-of-service information
    e.g. different routing to the same destination for high-bandwidth bulk traffic and for low latency real-time traffic

## Slide 19: Confusing..Not any more
By convention
Devices acting at the LAN layer and forwarding packets based on the LAN address are called switches (or, originally, bridges; some still prefer that term)
Deices acting at the IP layer and forwarding on the IP address are called routers.
Datagram forwarding is used both by Ethernet switches and by IP routers
  Destinations in Ethernet forwarding tables are individual nodes while,
  destinations in IP routers are entire networks (that is, sets of nodes)

## Slide 20: IP Routers
Notes: catchall

## Slide 21: Topology
So far…there are no loops… graph theorists might describe the network graph is acyclic, or is a tree
Loop-free network there is a unique path between any pair of nodes
  Forwarding-table algorithm
    every destination appears in the forwarding tables; the issue of choosing between alternative paths does not arise
No loops then there is no redundancy
  any broken link
    Partitioning the network into two pieces that cannot communicate
Redundancy is a good thing
  make decisions among the multiple paths to a destination

## Slide 22: Topology Contd…

## Slide 23: Traffic Engineering
Any intentional selection of one route over another, or,
any elevation of the priority of one class of traffic
Route selection can either be
  directly intentional,
  through configuration, or,
  can be implicit in the selection or tuning of algorithms that then make these route-selection choices automatically

## Slide 24: DVRP
Distance-Vector Routing-Update Algorithm
  Build forwarding tables on their own, but those tables are greatly influenced by the administrative assignment of link costs
  QoS example
At the LAN layer
  traffic-engineering mechanisms are historically limited, though, Software-Defined Networking
At the IP layer, more strategies are available

## Slide 25: Spanning Tree
A spanning tree is a subset of Graph G, which has all the vertices covered with minimum possible number of edges
A spanning tree does not have cycles and it cannot be disconnected

## Slide 26: Spanning Tree

## Slide 27: ST Properties
A connected graph G can have more than one spanning tree
All possible spanning trees of graph G, have the same number of edges and vertices
The spanning tree does not have any cycle (loops)
Removing one edge from the spanning tree will make the graph disconnected, i.e. the spanning tree is minimally connected
Adding one edge to the spanning tree will create a circuit or loop, i.e. the spanning tree is maximally acyclic

## Slide 28: Reading Assignment
Spanning tree
  TRILL
  SPB

## Slide 29: SDN
Software-Defined Networking
The core idea of SDN is to place the forwarding mechanism of each participating switch under the aegis of a controller, a user-programmable device that is capable of giving each switch instructions on how to forward packets
The controller can be a single node on the network, or can be a distributed set of nodes
The controller manages the forwarding tables of each of the switches

## Slide 30: SDN
Software Defined Networking (SDN) is changing the way we design and manage networks
  First, an SDN separates the control plane (which decides how to handle the traffic) from the data plane (which forwards traffic according to decisions that the control plane makes)
  Second, an SDN consolidates the control plane, so that a single software control program controls multiple data-plane elements

## Slide 31: Control-plane vs Data-plane

## Slide 32: Control-plane vs Data-plane
Control Plane = Learning what we will do
  Planning stage
    learning which paths the buses will take, is similar to the control plane in the network
    We haven't picked up people yet, nor have we dropped them off, but we do know the paths and stops due to our plan
    The control plane is primarily about the learning of routes.
  Routed network
    Planning and learning can be done through static routes
    Dynamic routing protocols, like RIP, OSPF and EIGRP to allow the routers to train each other regarding how to reach remote networks
    This is all the control plane.
Data Plane = Actualy moving the packets based on what we learned.
  Routers know how to route for remote networks
    comes a customers packet and BAM! this is were the data plane begins
  The data plane is the actual movement of the customers data packets over the transit path

## Slide 33: Historical Perspective
SDN
  How we design and manage Networks
  Making networks more programmable
  OpenFlow & Network O/S
SDN and NV
  Debunked common myths

## Slide 34: Road to SDN
Networks
  Routers
  Switches
  Middleboxes
    Firewalls
    NAT
    Load balancers
    Intrusion Detection Systems

## Slide 35: Road to SDN
S/W implements network Protocols
Network administrators
  configure individual network devices using configuration interfaces that vary
    across vendors
    and even across different
Network management tools
  offer a central vantage point for configuring the network
  Limitations
    Systems still operate at the level of individual protocols, mechanisms, and configuration interfaces
  This mode of operation has slowed innovation, increased complexity
  Inflated both the capital and operational costs of running a network

## Slide 36: Road to SDN
SDN has two defining characteristics
  First, an SDN separates the control plane (which decides how to handle the traffic) from the data plane (which forwards traffic according to decisions that the control plane makes)
  Second, an SDN consolidates the control plane, so that a single software control program controls multiple data-plane elements

## Slide 37: Control Plane
Makes decisions about where traffic is sent
Control plane packets are destined to or locally originated by the router itself
The control plane functions include the system configuration, management, and exchange of routing table information
The route controller exchanges the topology information with other routers and constructs a routing table based on a routing protocol, for example, RIP, OSPF or BGP
Control plane packets are processed by the router to update the routing table information.
It is the Signalling of the network
Since the control functions are not performed on each arriving individual packet, they do not have a strict speed constraint and are less time-critical

## Slide 38: Data Plane
Also known as Forwarding Plane
Forwards traffic to the next hop along the path to the selected destination network according to control plane logic
Data plane packets go through the router
The routers/switches use what the control plane built to dispose of incoming and outgoing frames and packets

## Slide 39: Example
R1, R2 and R3
  Telnet
  R1 and R3
    Control/management plane
  R2
    Data plane traffic

## Slide 40: Road to SDN
How does the control plane exercise its control over the state in the networks data plane elements?
  API
    OpenFlow
OpenFlow Switch
  has one or more tables of packet-handling rules
  each rule matches a subset of traffic and performs certain actions on the traffic that matches a rule
  actions include
    dropping
    forwarding
    Flooding
  Depending on the rules installed by a controller application
    OpenFlow switch can behave like a router, switch, firewall, network address translator, or something in between

## Slide 41: Road to SDN
Initial Vendors
  HP, NEC and Pronto
Controller platforms
  Beacon OpenFlow
  FloodLight
  NOX
  ONOS
  POX
  Nettle

## Slide 42: Road to SDN
Applications using these platforms
  Dynamic Access Control
  Server Load Balancing
  Network Virtualization
  Energy Efficient Networking
  Seamless Virtual Machines
  Migration and User Mobility

## Slide 43: Road to SDN
Commercial Success
  Google’s wide-area traffic-management system
  Nicira’s Network Virtualization Platform
Consortia
  Open Networking Foundation and
    https://www.opennetworking.org
  Open Daylight initiative
    https://www.opendaylight.org

## Slide 44: Road to Research in SDN
Evolution of key ideas
Application “pulls” and technology “pushes” of the day
Lessons that can help guide the next set of SDN innovations

## Slide 45: Roadmap